## Slide 1
Status Review
10.01.2018

## Slide 2: Last weeks:
Flushed each circuit with flushing device from Welkenrath (R407c)
Further work on the evaporator model
Changed the calculation method of the python script
Started writing

## Slide 3: Flushing of the cabinet
No oil in the circuits
Previous filling was
too high
(estimated 600ml
instead of 470ml)

## Slide 4: Evaporator model
Previous used equations are only valid for one-phase flow
Pressure drop equations changed  valid for 2-phase flow
ε-NTU method changed to fin correlations  αair
Assumptions:
  Xin =0
  Xout =1
  Inlet-Conditions: Tair, patm,uair,Trefr,prefr
  Δh known – equidistant cells
  Flow boiling
  Dry air
  => Goal is to see a trend of the evaporator performance

## Slide 5: Python script

## Slide 6: To-Do:
Test-Plan according to DoE
  Schedule Testing order
  Testing
  Representative Evaporator arrangements
  Parameters?
Evaporator | Condensor | TCOND | TDEFROST
Current arrangement | SWEPCURRENT | 55 | 4
LIDL-Design | SWEPSMALL | 45 | 3
V1 |  | 55 | 2
V2 |  |  | manual