## Slide 1
IDC R290 3x150g
Next Gen Solution
Project Update
Presenter: SB
Contributors: EW, PA, DD, KR
October 5th, 2017

## Slide 2: Gen2-150g - New Generation Integral Display Case Solution With Multi-Circuit Fixed Speed <150g
Technical Scope
Team
Timing & Status
Objectives
Solution package including
  Compressors (ZB*KAU)
  Flow controls (TX, PS)
  ECB-D Control Board
  Case design recommendations
    Evaporator Design
    Condenser Design
    Fans Control
    Accessories (Filters, …)
Complete Safety Concept w/ VDE & UL Approved parts
SB
KR/DD – Case Design Changes & Testing
EW/PA – Data Analysis & Design Evaluation
Sponsor: RD
Test: Baseline – Completed 03/07/2017
Modif: System Design Improvements – 18/07/2017
Test: 2nd campaign – Completed 28/08/2017
EBM-Papst workshop – 04/08/2017
Modif: ZB*KAU Hybrid Motor – 01/09/2017
Test: 3rd campaign – started 02/09/2017
Next steps
  Evaporator change – mid-October 2017
Develop NextGen Solution for R290 Display Case (150gr)
  Going beyond today design
    Applied cost
    Efficiency
  Improve design to achieve 3M1 requirements
Use AHT Vento Green 375 L8 as baseline
IP

## Slide 3: EN ISO 23953-2 Testing Requirements
Continuous setup improvement to get closer to ISO 23953 requirements.
Conditions | Current Status In Lab | Comments
Climate / Ambient conditions & measurement | OK | To be improved for full compliance w/ ISO 23933 (might lead to better results – tbc)
M-Packages Characteristics | OK | OK
M-Packages Temperature Measurement | Representative but reduced number of measurements points | Keep
Air movement accross cabinet ~ 0.2 to 0.1 m/s | Air speed in line with requirements (0.1 to 0.2 m/s) Air flow not in line w/ requirements but not disturbing significantly case operation (vizualized 19/07) | Improved w/ installation of « ceiling » (09/17). Need accurate speed measurement to adjust room fans speed (Oct 2nd)
Stability & Test period | OK (24hrs) | OK (24hrs is the minimum)
Power measurement | OK | OK
Water Temperature/Flow Control & Measurement | Not described by standard (35°C as reference?). Lidl requires 55°C Improved PID setting to better manage defrost transient (July 17th) | Some erratic behavior occurred. Solved. (Sept 2017) Switched to pure water for more accurate measurement (Aug 2017)
V

## Slide 4: Reminder July 2017 Baseline Test (Climate Class 3)
Lack of Capacity To Cool Down Products
3M1 (-1/+5) Requirements not fulfilled. Case achieved only 3H2 (-1/+10).
Case Front – Temperature Distribution
M1
M2
H2
Minimal Temperature
Case Back – Temperature Distribution
Test #05

## Slide 5: Reminder July 2017 Baseline Test (Climate Class 3)
Acceptable Efficiency Level – Main Limitation For System Efficiency Improvement Are Charge Limitation & Air Curtain
 |  | Average | Comments
T prod. max | °C | 10.2 | 
T prod. min | °C | 2.7 | 
T prod. Avg | °C | 6.4 | High products temperatures
T prod. median | °C | 5.8 | 
T air in | °C | 10.5 | High return air temperature
T air out | °C | 1.6 | 
Evap. Temp. | °C | -8.1 | 
Superheat | K | 13.7 | High superheat
Cond Temp. | °C | 34.0 | 
Liquid Quality | % | 16 | No liquid at condenser outlet
ΔT cond-water,out | K | -0.1 | Good condenser performance
Cooling Capacity | kW | 6.3 | Limited cooling capacity
Compressor COP | - | 2.4 | 

## Slide 6
Design Modifications & Results

## Slide 7: Summary Of Design Modifications
Phase 1 - Circuit
Phase 2 - Compressor
Phase 3 - Evaporator
Circuit Design Improvements
  Condenser w/ smaller internal volume (SWEP)
  New expansion valve
  Evaporator circuit optimization
  Variable Speed Fans
Control Improvements
  Demand defrost
New compressor design
  “Hybrid Motor”
Evaporator Design Improvements
  Internal volume reduction
  Optimal piping
  Distributor ?
100% Completed
80% Completed
Start Mid-October
Initial Design
Circuit
Optimization
New Design?

## Slide 8: Phase 1 – Results Impact of Circuit Design Modifications
Improved Circuit Design Allowed Better Use Of Evaporator & Better Cooling Down Of The Products
 |  | Baseline | Test 18 | Comments
T prod. max | °C | 10.2 | 10.7 | Lower products temperatures (-1.2°C in average)
T prod. min | °C | 2.7 | 0.5 | 
T prod. Avg | °C | 6.4 | 5.2 | 
T prod. median | °C | 5.8 | 4.7 | 
T air in | °C | 10.5 | 8.6 | Lower air temperatures
T air out | °C | 1.6 | -0.7 | 
Evap. Temp. | °C | -8.1 | -10.1 | 
Superheat | K | 13.7 | 9.0 | Lower superheat
Cond Temp. | °C | 34.2 | 34.8 | 
Liquid Quality | % | 16% | 11% | Still no liquid at condenser outlet
ΔT cond-water,out | K | -0.1 | -0.1 | Equivalent ΔT w/ less volume
Cooling Capacity | kW | 6.3 | 6.0 | Still limited cooling capacity
Compressor COP | - | 2.4 | 2.2 | No COP gain due to lower evap. temp.
Case Front – Temperature Distribution
Case Back – Temperature Distribution

## Slide 9: Phase 1 – Results Impact of (Modbus) Variable Speed Fans Control
Fans speed adjustment did not results in better cooling performance or efficiency. Air flow distribution & Air curtain are key.
Test w/ Unbalanced Speed Profile
  Result: No measurable improvement
  Reasons: 6 fans blowing in same open plenum. Working only in cases w/ modular evaporator design
  Solution: Would require significant modification of AHT design
Test w/ Lower/Higher Speeds
  Optimum is 1400rpm (nominal)
  Low speed  Product freezing
  High speed  Too high evap. Temp.
3
1
2
1
2
2
1

## Slide 10: Phase 1 – Results Impact of Demand Defrost Logic
Demand Defrost Allows To Run Defrost When It Is Required
Need More Tests To Quantify Benefit
Default (Today): Time Defrost
  Time interval (e.g. 3 to 4 hours) is usually optimized for one given operating condition
  Limitations: Defrost can start too late (coil fully frozen) or too early (unnecessary defrost). Impossible to tune for every store/climate/season.
Improved: Self-Learning Demand Defrost
  Principle: Detection is based on air-fin-product temperatures. Algorithm is learning
  Gain: Defrost is triggered when needed.
OK: 8°C evap
KO: evap -15°C
The right time for defrost
Patent Pending

## Slide 11: Phase 2 – Results Impact of Compressor Change
Calorimeter Testing (July 2017)
Gains resulting from motor change (“Hybrid motor”) and oil change (3MAF instead of HatCol)
Power decreases (especially at low condensing)
Slight capacity drop at high condensing. COP variation remains positive.
Display Case Testing
Similar operating conditions before & after (but no direct control)
No oil return issue
Questions:
  Does capacity drop impact case performance ?
  Does oil solubility variation impact case performance ?
  Variation in condenser performance ?
Efficiency gain due to lower power consumption is confirmed.
Further tests needed to evaluate potential impact of oil change
Condition SH10K/SC0K | P (W) | Q (W) | COP
-7/15°C | -16.6% | -0.2% | 19.6%
-7/35°C | -9.5% | -0.8% | 9.5%
-7/55°C | -4.2% | -3.1% | 1.2%
Condition Class 3 - 25°C/60% | P (W)
Low Condensing | N/A
Med. Condensing (Water 30/35°C) | -8.8%
High Condensing (Water 50/55°C) | -1.4%

## Slide 12: Phase 3 – Plan Evaporator Design Change
Evaporator Improvements
  Reduce effective pipe diameter (10mm to 7mm?) to reduce amount of charge in evaporator
    Not a limitation from suppliers (source: Karyer, LUVE, Guentner…)
    Limitation comes from OEMs (using std HFC coils)
  Increase counter flow effect
  Increase cross-flow effect by using more rows (4 instead of 2)
  Use distributor ?
Plan
  Finalize design change based on UPV’s inputs
  Use evaporator coil received from Lidl stock
    Same size & shape
    4 rows / 32 pipes (10mm)
    Not all pipes are used (flexibility)
  Reduce inner volume using “dead-volume”
Initial Design
Circuit Optimization
New Design?
FY18Q1

## Slide 13: External Information: Arneg – Brunel University 2011 Test Report – IDC 3.75m w/ R1270
Test report from Brunel University (London, UK)
3.75m Open Display Case (“Berlino”)
  Single air curtain + 6 fans
  2 circuits w/ Horizontal Hitachi DS1529S1
  R1270 (0.720 kg) – no charge optimization
Achieved 3M1 & 3M0 by optimizing panels design & air flow
Key Learnings
  3M0 & 3M1 achievable w/ open 3.75m case
  Cooling capacity need ~ 8 kW (@-7/30)
  Air Flow distribution & panel design is key
  COP: ZB*KAU vs Hitachi Scroll ~ +18%
  Display case test protocol
Note: Brunel University has long experience in Multideck Display case modelling, testing & optimization. Interesting potential partner for external design review/assessment.

## Slide 14: Conclusions & Next Steps
Fine-tune test setup (9th Oct)
  Room air speed adjustment
  Monitoring setup verification
Finalize current test campaign (“Hybrid Motors”) to validate results (Oct 16th)
Evaporator Change (Oct 23rd)
  To start second half of October
  Use available coil provided by Lidl as basis.
Refine Selection Of Expansion Device (Oct 23rd)
  Electronic valves are used for lab testing (flexibility)
External
  Get in touch w/ Burnel University for external design review (Oct 16th)

## Slide 15
backup

## Slide 16: EBM Variable speed Modbus fans Unbalanced fans speed control
Target: Improve temperature distribution in the cabinet
Results: no measurable improvement in terms of distribution nor avg product temperature
Reason: Common plenum after the fans equalizes static pressure and hence flow distribution through the honeycomb
Solution: Need to separate the fans per channel with baffles
Works only in the case of separate modular evaporators/circuits (confirmed by EBM Papst- Meeting 4Th of August)

## Slide 17: EBM Variable speed Modbus fans All fans from 1200 to 1800rpm
Qevap increases slightly with fan speed 1
Best product temperature at …1400rpm – same as fixed speed fan 2
T_a_out getting too low at low speed (risk of products freezing) 3
3
1
2

## Slide 18: Scope
Energy Efficiency
Look at total energy use (kWh) in continuous operation (24hrs)
Definitions (Lot12 & EN ISO 23953-2)
  TEC = Total Electrical Consumption [kWh]
  TDA = Total Display Area [m²]
  Eff = TEC/TDA = Case Efficiency [kWh/m²/day]
  EEI = Energy Efficiency Index = Eff/Eff_ref*100
Key Factors influencing efficiency
  Cabinet cross-section & configuration of shelves • the air flow configuration
  Lighting, night curtain, doors (closed cabinets)
  Evaporator & condenser design
  Refrigerant charge
  Compressor efficiency
  Superheat Control
  Fans efficiency & operation
  Defrost management
Case Temperature Category
Defined and certified according to EN ISO 23953-2
  Climate Classes (Ambiant Conditions)
    3: 25°C/60% (standard for Europe - LIDL requirement)
  Temperature class (Food Temperature)
    M1: Highest product < +5°C & Coldest product > -1°C (LIDL requirement)

## Slide 19: Test Setup
Display Case:
  AHT Vento 375 L8 – R290
Test Environment:
  Psychrometric Chambers A & B
  Case load w/ M-packages
Case Dimensions |  | Unit | Value
horizontal projection of the open surface | H0 | m | 0.2
cabinet lenght without end walls of the horizontal open surface | L0h | m | 3.76
horizontal projection of the glazing surface | Hg | m | 0
cabinet lenght without end walls of the horizontal glazing surface | Lgh | m | 3.76
vertical projection of the open surface | V0 | m | 1.55
cabinet lenght without end walls of the vertical open surface | L0v | m | 3.76
vertical projection of the glazing surface | Vg | m | 0
cabinet lenght without end walls of the vertical glazing surface | Lgv | m | 3.76
Total Display Area | TDA | m² | 6.58

## Slide 20: Case Design Improvements & Work Plan
-5/45/10K/0K |  | Baseline | Improved | Energy Efficiency | Temperature Class | Step 1 (July) | Step 2 (August)
Compressor | Motor | ZB09KAU | ZB09KAU* Hybrid Motor | +++ | 0 |  | V
 | Size |  | New displacement (+/- 20% w/ inverter) | 0 | 0 (?) | V | 
 | Oil | HatCol | 3MAF | ++ | 0 |  | 
 | Free Volume | Standard | -50% | ++ | ++ |  | Feasibility
Fans |  | Fixed Speed | EC Fans | ++ | + (?) | V (Trial & Error) | 
Filter Drier |  | Danfoss DML 1.52X2/2S | Parker | 0 (?) | 0 (?) |  | 
Condenser - PHX | Type | Danfoss D22-20 | SWEP (20) | + (?) | + (?) | V | 
Evaporator Coil | Configuration | Original | Parker Distributor 1-to-3 | + (?) | 0 (?) |  | 
 | Model | Original | New Design | + (?) | + (?) | Design w/ manufacturers | Test
 |  |  | Improved counteflow effect |  |  |  | 
Expansion Valve | Type | Honeywell TLK-E1016 | TIH or TX3 (variable w/ EXM) | N/A | N/A | V EXM-BOE | 
 | Location | Evaporator Inlet | Condenser Outlet | + | + |  | ??
Air Flow Distributors |  | Today Air Curtain | Improved (Trial and error) | + (?) | + (?) | V (Trial & Error) | 
Defrost Control | Demand Defrost Control |  |  | + | 0 |  | 
Room Upgrade | Air flow & Water Flow management |  |  |  |  | Evaluate & Quote | 
Focus on achievable inner volume reduction, air distribution & efficiency improvements. Impact on temperature class is hard to predict and will be evaluated during tests

## Slide 21: ZB*KAU - Compressor Design Improvements
High Side ~ 14gr R290
Free Volume 0.34L
Low Side ~ 12gr R290
Free Volume 1.62L
Refrigerant diluted in the oil ~ 37gr for 0.74L
Decreasing free vol. 95% (direct discharge) could gain about 13gr.
/!\ Pulsations in discharge line
Decreasing free vol. 50% could gain about 6gr
Oil charge has been reduced from 0.74L to 0.47L
Reduction of R290 diluted in oil from 37g to 23.8g
V
Hybrid Motor
Oil Change
Hatcol4467 to 3MAF
ΔCOP +4.3% to +1.1%
Cost Reduction
ΔDilution +3%
ΔCOP > +5%
Done
On-Going (Release Nov 2017)
Done
Energy Efficiency Gains
R290 Charge Improvements

## Slide 22: EC Fans
EC (Variable Speed) Fans Being Implemented
Target to improve temperature distribution in the cabinet
Objective
  Unbalanced fans speed control for improved temperature distribution in DC
Existing: K1G200-AA89-12 (Two-speeds 1200-1400rpm)
New: K1G200-AA60-XN (EC Fans – up to 1800rpm)
Notes:
  Decision to keep current fan-evaporator configuration (fans on top – coil at bottom)
  NDA w/ ebm-papst under preparation
  Emerson-EbmPapst workshop scheduled in AAC (August 4th, 2017)

## Slide 23: Refrigerant Charge Gains & Losses
Focus On Changes Bringing Charge Gains.
Need To Quantify Gain & Feasibility of Compressor Design Improvement
Component | Before | Alternative | Delta / % on 150g
Compressor - free volume | 22.9 g | 11.5g | -11.4g / -7.6%
Compressor - oil dilution | 0.47L Hatcol 23.8 g | 3MAF 24.6 g | +0.8g / +0.5%
Filter Drier | 16.5g | ALCO: 33.0g | +16.5g / +11.0%
 |  | Parker: | Equivalent ?
Condenser (liquid 35%) | 35.5g | SWEP x28: 48.0g | +12.5g / +8.3%
 |  | SWEP x20: 32.0g | -3.5g / -2.3%
Liquid Line (move up TXV up) | 8.2g | 2.4g | -5.8g / -3.9%
Evaporator (liquid 30%) | 145.2g | With distributor | To be evaluated/tested
New evaporator design |  |  | To be evaluated/tested
Condition: -5°C EVAP, 45°C COND, 10K SH, 0K SC

## Slide 24: New Evaporator Design – Status
Evaporator Coil Specification established based on baseline results
  General requirements first
  Provide more info on current design upon request
Supplier | Circuits | Distributor | Length | Tube Diameter | Tube Thickness | Row x column | Fin Space | Tubes Surface | Internal Volume | Comment
Original (KARYER-AHT) | 3 | NO | 3.4 | 10mm |  | 9 x 2 (16 x 2) | 5mm | 0.64m² | 1.30 l | Standard HFC design
Modified (KARYER-AHT) | 3 | NO | 3.4 | 10mm |  |  | 5mm | 0.64m² | 1.30 l | Improved Counterflow effect
EPTA – SEST | 3 | YES | 2.3 | 7mm |  | 12 x 4 |  | 1.21m² | 1.67 l | EPTA – NDA (Confidential)
REFRION (via ROLLER) | 3 | NO | 3.4 | 10mm |  |  |  | 0.61m² | 1.28 l | No improvement expected
LUVATA |  |  |  |  |  |  |  |  |  | 
Thermofin | 3 | YES | 3.4 | 5mm |  | 20 x 6 | 4mm? | 2.14 m² | 2.07 l | Prototype to be ordered 6 weeks lead time
Sierra |  |  |  |  |  |  |  |  |  | New [EW]
HTS / LUVE |  |  |  |  |  |  |  |  |  | New [EW]
GUETNER |  |  |  |  |  |  |  |  |  | On-Hold
Friterm |  |  |  |  |  |  |  |  |  | New [FR]
TO BE UPDATED

## Slide 25: Evaporator Design Improvement
Current Design
Proposed Design
Distribute each circuit 3 times to two passes
  shorter pipe length per circuit
  Lower velocity
Target reduction of pressure drop & increased evaporator effectiveness
3 circuits with 6 passes
long evaporator pipe length per circuit
  high pressure drop
Expected positive impact on efficiency
Impact on cooling capacity is hard to predict (Test Needed)

## Slide 26: Fan Curve Assuming Sensible Heat Exchange Only
Baseline (#5) – K1G200-AA89-12 (1400rpm)
  Power (6 fans): 70.95 W – 11.83 W/fan
  Flow: 0.52 m³/s – 1868 m³/h
Baseline (#45Hz) – K1G200-AA89-12 (1400rpm)
  Power (6 fans): 70.81 W – 11.80 W/fan
  Flow: 0.51 m³/s – 1810 m³/h
New (#18) - K1G200-AA60-XN (1400rpm)
  Power (6 fans): 74.28 W
  Flow: 0.42 m³/s – 1508 m³/h

## Slide 27: EBM-Papst – Emerson / Meeting notes (August 4th, 2017)
Comments
  Unbalanced fan speed distribution can help if air « channels » are properly separated. In current design, all fans are blowing through a « plenum » so unbalanced fan speed is not bringing significant improvement. « Plenum » effect is enhanced by the « wafel » plate
  Diagonal fans help because of less « directed flow »
  Current configuration (fans « sucking » air through coil) is better from an air distribution point of view
  Mixed-flow (diagonal) flow have steeper Pa-qv flow characteristic curve  flow is less sensitive to pressure drop variation (e.g. frost formation)
  Deflector behind honeycomb might be optimized. Evaluate possibility to remove it or re-position it (change curvature?)
  Benefit/effect of double air curtain is confirmed based on Ebm-Papst experience
  Compressor box is blocking a significant section of air channel
    Sharp edges should be avoided
    Increase speed & isolate section could help compensating this effect and increasing the flow
Actions
  Store plenum & opened case pictures on server (KR)
  Check recommendations in ISO 23953-2 about m-pack position (e.g. distance from panels or shelf border)
  Need to consolidate test data (evaporator heat transfer balance) to estimate fan operating point
    Averaging period has some impact due to frost formation
    Go-back to Ebm-Papst team to evaluate w/ fans characteristic curves
  Air curtain seems perturbated at the bottom and « pushed » from the back of the case. Need to evaluate impact of speed at air inlet (e.g. increase by reducing cross section) and air « injection » from the back panel
  Evaluate possibility to provide 3D drawings to Ebm-Papst to run CFD simulations
  500gr project: Get back to Ebm-papst w/ fan specification of ELCO fans for selection of EC-fans (axial fans would remain better here)

## Slide 28: Filter Drier Alternatives

## Slide 29: Relevant Standard - EN ISO 23953
Coding Definition
  Over 100 types & configurations
  Example : IVC2 (Integral – Vertical – Chilled products – Multi-deck)
Definitions
  Climate Classes (Ambiant Conditions)
    0: 20°C/50%
    8: 24°C/55%
    3: 25°C/60% (standard for Europe - LIDL requirement)
  Temperature class (Food Temperature)
    M1: Highest product < +5°C & Coldest product > -1°C (LIDL requirement)
    M2 : Highest product < +7°C & Coldest product > -1°C
    H2 : Highest product < +10°C & Coldest product > -1°C
  Energy Consumption
    TEC = Total Electrical Consumption [kWh]
    TDA = Total Display Area [m²]
    Eff = TEC/TDA = Case Efficiency
    EEI = Energy Efficiency Index = Eff/Eff_ref*100